## Slide 1
Module 8.6
Link-layer and TCP/IP connectivity

## Slide 2: 802.11i Protocol (WPA2)
Authentica-tion Server (RADIUS)
No Key
Authenticator UnAuth/UnAssoc
802.1X Blocked
No Key
Supplicant
UnAuth/UnAssoc
802.1X Blocked
No Key
Supplicant
Auth/Assoc
802.1X Blocked
No Key
Authenticator Auth/Assoc
802.1X Blocked
No Key
Authentica-tion Server (RADIUS)
No Key
802.11 Association
EAP/802.1X/RADIUS Authentication
Supplicant
Auth/Assoc
802.1X Blocked
MSK
Authenticator Auth/Assoc
802.1X Blocked
No Key
Authentica-tion Server (RADIUS)
MSK
MSK
Supplicant
Auth/Assoc
802.1X Blocked
PMK
Authenticator Auth/Assoc
802.1X Blocked
PMK
Authentica-tion Server (RADIUS)
No Key
4-Way Handshake
Supplicant
Auth/Assoc
802.1X UnBlocked
PTK/GTK
Authenticator Auth/Assoc
802.1X UnBlocked
PTK/GTK
Authentica-tion Server (RADIUS)
No Key
Group Key Handshake
Supplicant
Auth/Assoc
802.1X UnBlocked
New GTK
Authenticator Auth/Assoc
802.1X UnBlocked
New GTK
Authentica-tion Server (RADIUS)
No Key
Data Communication
Supplicant
Auth/Assoc
802.1X UnBlocked
PTK/GTK
Authenticator Auth/Assoc
802.1X UnBlocked
PTK/GTK
Authentica-tion Server (RADIUS)
No Key
Link Layer
Notes: RSNA involves three entities: the Supplicant, the Authenticator, and the Authentication Server. In an general infrastructure network, the supplicant is implemented in the mobile devices like a PDA, a cellphone or a laptop; the authenticator is implemented in the Access Point; the authentication server could be implemented either in the Access Point with the authenticator, or separately in a backend server, like a RADIUS server. When it is implemented in a separate server, the links between the authenticator and the authentication server are assumed to be physically secure.
In order to adopt 802.1X authentication in wireless networks, we consider the association between the supplicant and the authenticator as a logical 802.1X port. At the beginning, the supplicant and the authenticator are unauthenticated and unassociated, 802.1X ports are blocked, and there are no shared secrets between them.
In the first stage, the supplicant and the authenticator set up an 802.11 association. After this stage, the supplicant and the authenticator go to the authenticated and associated state. Here “authenticated” only means that 802.11 open system authentication is successful, this is not considered to be a real authentication. Now there is a radio connection between the supplicant and the authenticator, but they cannot transmit data packets to each other because the logical 802.1X port is still blocked, only protocol packets are accepted.
In the second stage, the authenticator will act as a relay, the supplicant and the authentication server run some mutual authentication protocol and generate some common secret, called MSK (Master Session Key). Then the server moves the MSK to the authenticator, and the supplicant and authenticator will derive the same PMK (Pair-wise Master Key) from the MSK locally. Here “move” means the server will delete the key itself after sending to the authenticator, because the server is assumed not to disclose and possess the key afterwards. This stage could be absent when a Pre-Shared Key or a cached PMK is used.
In the third stage, the authenticator initialize a 4-way handshake to confirm the PMK existence and derive a fresh PTK for the following data sessions. Upon this point, the 802.1X ports are unblocked to accept data packets.
As the fourth stage, the supplicant and the authenticator might also perform a group key handshake to distribute a GTK in case of multicast applications, however, this is not necessary since the GTK (Group Transient Key) could also be transmitted in the 4-way handshake.
With the shared PTK and GTK, the supplicant and authenticator could derive the encryption key and MAC key, thus perform secure data communications.
We will focus on the 4-way handshake because it is an essential part in all operation modes.

## Slide 3
TCP/IP connectivity

## Slide 4: Basic Layer 2-3 Security Problems
Network packets pass by untrusted hosts
  Eavesdropping, packet sniffing
  Especially easy when attacker controls a machine close to victim
TCP state can be easy to guess
  Enables spoofing and session hijacking
Transport layer security

## Slide 5: Virtual Private Network (VPN)
Three different modes of use:
  Remote access client connections
  LAN-to-LAN internetworking
  Controlled access within an intranet
Several different protocols
  PPTP – Point-to-point tunneling protocol
  L2TP – Layer-2 tunneling protocol
  IPsec (Layer-3: network layer)
Data layer

## Slide 6
Credit: Checkpoint

## Slide 7: IPSEC
Security extensions for IPv4 and IPv6
IP Authentication Header (AH)
  Authentication and integrity of payload and header
IP Encapsulating Security Protocol (ESP)
  Confidentiality of payload
ESP with optional ICV (integrity check value)
  Confidentiality, authentication and integrity of payload

## Slide 8: Recall packet formats and layers
Application
Transport (TCP, UDP)
Network (IP)
Link Layer
Application message - data
TCP
data
TCP
data
TCP
data
TCP Header
data
TCP
IP
IP Header
data
TCP
IP
ETH
ETF
Link (Ethernet)
Header
Link (Ethernet)
Trailer
segment
packet
frame
message

## Slide 9
IPSec Transport Mode: IPSEC instead of IP header
http://www.tcpipguide.com/free/t_IPSecModesTransportandTunnel.htm

## Slide 10: IPSEC Tunnel Mode

## Slide 11
IPSec Tunnel Mode: IPSEC header + IP header

## Slide 12: IKE subprotocol from IPSEC
A, (ga mod p)
B, (gb mod p)
Result: A and B share secret gab mod p
A
B
m1
m2
, signB(m1,m2)
signA(m1,m2)
Key management